## Slide 1: MPG
General Purpose Input/Output
(GPIO)

## Slide 2: Housekeeping
Sub next week
Feb 10 = Family Day
Feb 17-21 = Reading Break
www.engenuics.com
Attendance

## Slide 3
Notes: Here’s the pinout of the MPG processor. You can see JTAG, LCD backlight, LEDs, buttons, buzzers, Blade (I2C, SPI, ADC, UART), Debug UART, ANT (SPI), HSMCI (SD card), USB

## Slide 4
Notes: Since we’re working with a general-purpose microcontroller, every pin needs to be configured for our application and circuit

## Slide 5
xxER = Enable Register
xxSR = Status Register
xxDR = Disable Register
Pull-up
Set/Clear Output
Input/Output
Peripheral
Peripheral A/B Select
Notes: The output sections. Note the common ER / SR / DR endings

## Slide 6
xxER = Enable Register
xxSR = Status Register
xxDR = Disable Register
Status
Debounce/Glitch
Interrupt enable/mask/status
Notes: Input sections

## Slide 7: GPIO notes
Almost all processors default to “input” on power-up
  This means that it won’t drive high/low and fry anything
Most processors have multiple “ports” (GPIOA, GPIOB, etc.) so they can have more than 32 pins
Some processors have a single “enable/disable/status” register, which means that you have to read/modify/write
  Causes problems if the processor interrupts in the middle…
  Our processor has separate registers so you can just write
You always have to refer to the processor’s reference manual
I always do the pin setup as the first thing in a project

## Slide 8: CPU Registers and Structs
(this isn’t even half of the GPIO registers)
Notes: Embedded Programming is all about taking all of the CPU registers and hiding them away into APIs useful for your application, then building a program on top of that.

## Slide 9: CPU Registers
ALL CPU registers are just values written to or read from special memory addresses!

## Slide 10: CPU Registers
void GpioInit(void)
{
*((u32 *)0x400E0C00) = 0x84030107;
…
}
#define PIO_PERA (*(u32 *)0x400E0C00)
#define MPG_PERA (0x84030107)
void GpioInit(void)
{
PIO_PERA = MPG_PERA;
}
Notes: Do you really want to go through defining all of these constants?
0x84030107 isn’t very clear … it’s like a “magic” number that would take a while to figure out and debug or correct if we ever had problems

## Slide 11: Structs (revisited)
typedef struct
{
u16 lengthPixels;
u16 widthPixels;
} RECTANGLE;
u32 Area(RECTANGLE const *pRectangle)
{
return (u32)pRectangle->lengthPixels * (u32)pRectangle->widthPixels;
}
void ShrinkToSquare(RECTANGLE *pRectangle)
{
if (pRectangle->lengthPixels <= pRectangle->widthPixels)
pRectangle->widthPixels = pRectangle->lengthPixels;
else
pRectangle->lengthPixels = pRectangle->widthPixels;
}

## Slide 12: Structs
typedef struct
{
u16 lengthPixels;
u16 widthPixels;
} RECTANGLE;
u32 Area(RECTANGLE const *pRectangle)
{
return (u32)pRectangle->lengthPixels * (u32)pRectangle->widthPixels;
}
void ShrinkToSquare(RECTANGLE *pRectangle)
{
if (pRectangle->lengthPixels <= pRectangle->widthPixels)
pRectangle->widthPixels = pRectangle->lengthPixels;
else
pRectangle->lengthPixels = pRectangle->widthPixels;
}
int main(void)
{
RECTANGLE rec = {2, 4};
u32 recArea = Area(&rec);
ShrinkToSquare(&rec);
u32 sqArea = Area(&rec);
…
}

## Slide 13: Structs
typedef struct
{
u16 lengthPixels;
u16 widthPixels;
u32 colorRgb;
} RECTANGLE;
0x0000 | lengthPixels
0x0001 | 
0x0002 | widthPixels
0x0003 | 
0x0004 | colorRgb
0x0005 | 
0x0006 | 
0x0007 | 
0x0008 | 
Continuous block of memory

## Slide 14: Structs
Address | name | offset (bytes)
0x4F02_0340 | lengthPixels | 0
0x4F02_0341 |  | 
0x4F02_0342 | widthPixels | 2
0x4F02_0343 |  | 
u32 Area(RECTANGLE const *pRectangle)
{
return (u32)pRectangle->lengthPixels * (u32)pRectangle->widthPixels;
}
int main(void)
{
RECTANGLE rec = {2, 4};
u32 recArea = Area(&rec);
…
}
rec
0x4F02_0340
Read the value at (0x4F02_0340 + offset 0)
-> offset
-> offset
Read the value at (0x4F02_0340 + offset 2)
(&struct – just the address of the first member in the struct)

## Slide 15: CPU Registers and Structs
typedef struct {
u32 PIO_PER;
u32 PIO_PDR;
u32 PIO_PSR;
u32 Reserved0;
u32 PIO_OER;
u32 PIO_ODR;
u32 PIO_OSR;
u32 Reserved1;
u32 PIO_IFER;
u32 PIO_IFDR;
u32 PIO_IFSR;
u32 Reserved2;
u32 PIO_SODR;
u32 PIO_CODR;
u32 PIO_ODSR;
u32 PIO_PDSR;
} AT91S_PIO;
#include “AT91SAM3U4.h”
Notes: Half of the registers for the PIO

## Slide 16: CPU Registers and Structs…
typedef struct {
volatile unsigned int PIO_PER;
…
} AT91S_PIO;
#define AT91C_BASE_PIOA ((AT91S_PIO *)0x400E0C00)
#define AT91C_BASE_PIOB ((AT91S_PIO *)0x400E0E00)
void GpioInit(void)
{
  AT91C_BASE_PIOA->PIO_PER = …;
  }
Notes: Is everyone with me? Have I lost anyone?
Still – let’s go a little further and see how we can make the value that is read/written clearer…

## Slide 17: Register Bits
Port B, P14
Port B, P13
Port A, P17
Port B, P0

## Slide 18: Register Bits
How would you make the button easier to use in code (besides 0x00000001)?
#define GPIO_BUTTON1 BIT0 // What about GPIOA vs GPIOB?
#define GPIOB_BUTTON1 BIT0 // Better… but still easy to mix up
#define GPIO_BUTTON1 GPIOB, BUTTON1 // Means 2 values for each pin…
PortA = {0 – 31} PortB = {32-63} enumerator! …

## Slide 19: GPIO Enum
typedef enum
{
  GPIO_PIN_PA0, // 0
  GPIO_PIN_PA1, // 1
  …
  } GPIO_PIN;
  void GpioSet(GPIO_PIN pin)
  {
  if (pin < 32)
  GPIOA->PIO_SODR= (1 << pin);
  else
  GPIOB->PIO_SODR= (1 << (pin & 0x32));
  }

## Slide 20: GPIO Enum
static AT91S_PIO * const pGpioReg[] = { GPIOA, GPIOB };
#define GPIO_PIN_PORT(pin) (pin >> 5) // or divide by 32
#define GPIO_PIN_BIT(pin) (1UL << (pin & 31))
void GpioSet(GPIO_PIN pin)
{
u32 port = GPIO_PIN_PORT(pin);
u32 pinBit = GPIO_PIN_BIT(pin);
pGpioReg[port]->PIO_SODR = pinBit;
}

## Slide 21: GPIO Enum
#define _BIT(n) (1U << (n))
GPIOA->PIO_OER = (_BIT(GPIO_LED_GREEN) | _BIT(GPIO_LED_RED) | …);
…
actual code use something called “x-macros” to simplify this step… too much to get into explaining today!

## Slide 22: Your Turn!
void GpioClear(GPIO_PIN pin);
void GpioSetState(GPIO_PIN pin, bool pinState);
void GpioToggle(GPIO_PIN pin);
bool GpioIsSet(GPIO_PIN pin);
TortoiseSVN -> Switch:
/SAM3U/MPGL1/Exercises/GPIO